Introdução

Este documento possui o objetivo de especificar um framework capaz de controlar a trajetória de um robô não omni direcional.

Objetivo

O objetivo deste projeto é criar um framework capaz de controlar a trajetória de um robô, de forma que possa ser reusado por outros programas e torne o controle de trajetória transparente.

Contexto

Este projeto possui no seu contexto um robô com interfaces de hardware (atuadores, sensores) e software (ROS Nodes) .
O nó do ROS chamado RosAria é quem possui as infoirmações relacionado aos atuadores e sensores, e o nó do ROS chamado controlador de trajetória irá se utilziar das informações contidas no RosAria para controlar a trajetória do robô.

Diagrama de implantação

Diagrama de componente

### RosAria
Simple node that uses ARIA to control the robot
#### Subscribed Topics
cmd_vel (geometry_msgs/Twist)
receives new velocity commands. Desired velocities are set in ARIA; the robot will achieve and maintain these velocities, so cmd_vel commands are only needed to change velocity, not maintain them.
#### Published Topics
pose (nav_msgs/Odometry)
publishes odometry information (rate depends on the robot, normally 10Hz)
bumper_state (rosaria/BumperState)
publishes bumper states (thanks to Arturo Ribes of the Spanish National Research Council)
sonar (sensor_msgs/PointCloud)
publishes sonar readings (thanks to Michiel Blokzijl of the Imperial College London). Readings are taken if there are subscribers on the topic. When the last subscriber unsubscribes from both this and sonar_pointcloud2 topic, sonars are turned off. Only available on robots with sonar. The point cloud is two dimensional, and its coordinate frame matches the robot position. X and Y are points on the plane of the robot. Z data is always 0.
sonar_pointcloud2 (sensor_msgs/PointCloud2)
publishes sonar readings as sensor_msgs/PointCloud2 type. Readings are taken if there are subscribers on the topic. When the last subscriber unsubscribes from both this and sonar topic, sonars are turned off. Only available on robots with sonar. The point cloud is two dimensional, and its coordinate frame matches the robot position. X and Y are points on the plane of the robot. Z data is always 0.
battery_state_of_charge (std_msgs/Float32)
Battery state-of-charge percentage, range (0.0, 1.0). Only published if robot type supports state of charge (e.g. Pioneer LX, Seekur, Seekur Jr.)
battery_voltage (std_msgs/Float64)
Battery voltage measurement (DC volts).
battery_recharge_state (std_msgs/Int8)
Recharging status. Only published on Pioneer LX robot. 0 if not charging, > 0 if recharging, and < 0 on error or no data.
motors_state (std_msgs/Bool)
Indicates whether the motors are enabled (true) or disabled (false). (You can use the enable_motors and disable_motors services to enable/disable the motors.)
#### Services
enable_motors (std_srvs/Empty)
Enable the motors. May be used to re-enable motors if automatically disabled by an event such as e-stop button or bumper hit. ROSARIA initially enables the motors after connecting to the robot. Some robots (Seekur, Seekur Jr.) also have a separate physical MOTORS switch that must also be turned on.
disable_motors (std_srvs/Empty)
Disable motors. Depending on the robot this may just disable motion commands, or it may also switch off power to the motors. Use the enable_motors service to re-enable them.

Requisitos fucnionais e não funcionais